| Lots of close buckets errors | Increase w bucket opening – see 8 check springs or buildup in opening |
| --- | --- |
| Different weights in one row | Increase accum bucket minimum to 6% - see 9 Or adjust air for discharge chute |
| To calibrate bucket | Power off, power, E, F4,F4, F3 9753 |
| To test opening doors – teflon plates | Power off – power, E, F4, F2, F1, F1, 3891 E arrow down to Y40, hit E repeatedly |
| To power off | Hit Power (X) and then in a few seconds, hit 0 |
| To power on | Hit Power (X) and then E |
| To start program | Power, E , F1, select program number, E, E |
| To change w bucket opening | F3 arrow to w bucket, enter #, E |
| To change accum bucket | F3, arrow to Ac bucket, enter #,E |
| If teflon plates stay down … | Scrape top to fill clicking buckets see #26 & #23 |
| To shut off incline belt | F + 4 then F + 4 to turn back on |
| To empty all for supper | F + 9 then when done, power off |
| To empty machine , not belt | F + 4, then F + 9 |
| Chicken is 13089 Turkey is 13091 Beef is 13090 | Program 1 & 89 Program 3 & 91 Program 2 & 90 |
| Lots of rejects caused by | Charge bucket open, or frozen chunks |
| Press K to | Stop Line (if bilw. Are enabled on panel) |
| To disconnect a channel (bucket) | Press E, F4, F4 use arrow keys, E to shut off and on |
| To return to prev. screen | C as many times as necessary |
| Manual Taring | E, F1, G, press channel or F4 for all |
| To Recalibrate Cone | Pwr off,pwr,E, F4, F1, E, null, E, add wt., E,adusted |
| Keep Dosage Vibrator @ 70-90 | By adj dosage time >time lowers dos vibrator Decrease time increases dos vibrator |
| Passwords | 3891 9753 1983 |
| To clean with power off Make sure meat drops centrally Deviation To adust amount on incline belt No Meat in 2 front pies Hit F & 8 end of night | Power on with X, then 0 to open all buckets Or move incline belt E F3 F1 E E then C F2 arrow up enter new number E, C, C Unplug chute with poker To finish meat when machine is getting empty |

| F2 Speed | Dosage Vibrator 70-90 |
| --- | --- |
|  | Storage Vibrator 65 - 90 |
|  | Centre Hopper 55 |
| F3 Time | Weigh Bucket open 2 - 5 |
|  | Dosage Time 3-10 adjust to keep dosage vibr betw 70 – 90 |
|  | Centre Pause 7 |
|  | Centre Pulse 35 |
|  | Accum. Bucket 6 ,7 or 8 |
|  | Reject Time 15 |
| F1 Stoppts | Product Layer Centre 30-40 |
|  | Minimum Layer Cente 50 - 60 |

Problem: Cannot change stoppts from 0	Solution: Recalibrate Cone see # 22 also check timers 118 & 119 to see if they have reverted to zero

Problem: Incline belt not stopping ESP #2 	Solution: Use air hose to blow water out of plug (level with floor of walkway)

# Problem: Bilw very slow, rejecting lots Solution: Check stable width (various) feb 18-03 <bilw#1 is1.6 bilw#2 is .6> also check 118 & 119

Problem: Rejecting empty doses	Solution: Shut off one bucket @ time and watch for 1 minute to see which bucket is faulty or recalibrate or check with wt.

# For a helpful hint about any present screen push ?Y

# Timers

> # 119 to stop double dumping or one gate not opening (esp in bilw 2) 	< to speed up line

While in program, E, F4, F1, F1, arrow down 5X, arrow right 1X, E, 1 9 8 3 , E  input new number (move by 5’s), E, C, C 	(#1 usually set at 30 while #2 is usually 45 – 60 ) - 60 being slowest

## Printers Parameters

# Reg Pies POTPIE15		  Club Pk Pies		    Club– Packing Rm

Forward Margin 40 (30)	/	30 (30)	 <40>		/		60

R Margin	  75 (90)	/	160(170)<160>	/		43

Speed 		900		/	900			/		350

Spacebar to select enter 2X to use the new setting (close selection to change screens if in editing)

| Stamp DEC04 12153 For Dec 15,2003 |
| --- |
| Club Pk Code Pk Rm 4 pk 15DEC2004 15123N 55B Time |
| Front | 15DEC2004 12153 55B 5 Time |

Before Supper: Servicer brings tank & plastic to Lites

Lites/Bilwinco empties billies and returns meat to cooler

SQC calls supper @ 67 and calls amerios 3262

After Supper: Servicer & Lites each bring one tank of meat

Break SQC calls break @ 67 and calls amerios 3262

End of Night: SQC Washes scales, poker, spoons, scrapers, glaze b.,etc. Locks both cupboards Photocopy weight sheet and hand in Servicer Returns thermometer, washes tools, returns tools to locker, gives tank and plastic to lites pink sheet, hand in dough sheet & pwith pink sheet, hand in dough sheet & pink tags Lites/Bil Empties billies, Return meat to cooler after weighing, hand in meat sheet with returned wt & metal check sheet Panel Finishes off & shuts down computer, take & erase count, write count in book, hand in downtime (&photocopy), Cartons Returns 3 lockout tags to cupboard

February 20, 2003